## Slide 1: Design and Fabrication of a Deep-Space Habitat Mockup for Human/Robot/System Interaction Research
By Angel Rodas
Human/Robotics/Vehicle Integration & Performance Laboratory

## Slide 2: About the Speaker
Name: Angel Rodas
NSF CAMP Scholar
Mechanical and Aerospace Engineer
Project Lead of the Deep-Space Habitat Mockup
Designing and Building an Off-Earth Habitat Mockup on Earth!
Notes: -Keep it general we will get more specific in the following slides
-Say Personally you see yourself as Science Student, Engineering Enthusiast, and Aerospace Aficionado
-Mention that the project you will be discussing is the Deep Space Habitat Mockup.
-Mention your fascination with flying machines and space since watching Star Wars and Top Gun as a child.

## Slide 3: About H.O.M.E
Habitats Optimized for Missions of Exploration
NASA Space Technology Research Institution
Collaborative effort involving multiple universities and commercial partners
Developing Next-Gen Space Exploration Technology
Lessen Reliance on Earth
Following Photos Courtesy of NASA...
Notes: -Keep it general we will get more specific in the following slides
-Say Personally you see yourself as Science Student, Engineering Enthusiast, and Aerospace Aficionado
-Mention that the project you will be discussing is the Deep Space Habitat Mockup.
-Mention your fascination with flying machines and space since watching Star Wars and Top Gun as a child.

## Slide 7: Current Efforts
Developing Autonomous Robotic collaboration technology
Life Support Systems
Machines to improve quality of life in space
HRVIP Lab
Notes: -Mention that they have a whole list of what research they are doing and when listed on the HERA page of the NASA website.

## Slide 8: Similar Research and Facilities
Human Exploration Research Analog (HERA)
CU Boulder HOME Mockup​
Notes: HERA
Behavioral health and performance studies
Communication and autonomy studies
Human factors evaluations
Medical capabilities assessments
Cu Bolder
Investigate human health and performance
Develop environmental control systems

## Slide 9: Our Research
Human/Robot/System Interaction Research
Notes: -Mention that they have a whole list of what research they are doing and when listed on the HERA page of the NASA website.

## Slide 10: Requirements
Build a durable, safe, and easily maintainable simulated deep space habitat which is affordable and accessible
Give researchers and subjects a low-risk and low-cost platform to improve solutions to the challenges of operating in a deep space habitat
Notes: -Explain who the all is, Institutions, Organizations, or groups that wish to test their protocols, experiments, and psychology in as close to a space like environment without the risk or expense of going to space.
-Challenges include but are not limited to: Isolation, Confinement, remote environment, communication delay, communication loss just to name a few.

## Slide 11: Solutions
Designed to be modular (easily reconfigured, upgraded, and expanded)
Disassembled and reassembled with Minimal Work
Can be assembled for years at a time
Well-documented, easily repeatable design for future expansion
Reasonable price for construction and maintenance

## Slide 12: Our Design

## Slide 13: Discussion
We started with the frame
The frame is made of 80/20 Aluminum
Floor can hold 1500lbf and fit 7 people with 3 ft of space each
Notes: -Explain because it is the most logical place to start. Dictates the Interior design in terms of usable space.

## Slide 14: Discussion
Semi-Cylindrical exterior shell
Shell is made of Fiber Reinforced Plastic (FRP)
Notes: -Explain because it is the most logical place to start. Dictates the Interior design in terms of usable space.

## Slide 15: Discussion
8 Panels connected with plastic H Channels
Notes: -Explain because it is the most logical place to start. Dictates the Interior design in terms of usable space.

## Slide 16: Discussion
Wooden formers attach the FRP to the 80/20 Aluminum Structure
Bottom Former
Top Former​
Notes: -Explain because it is the most logical place to start. Dictates the Interior design in terms of usable space.

## Slide 17: Discussion
8x2x2 Lateral Beams Provide Support to the FRP shell
Maximizes interior volume and provides utility
Notes: -Explain because it is the most logical place to start. Dictates the Interior design in terms of usable space.

## Slide 18: Discussion
8x2x2 brackets are slotted to account for wood dimension variability

## Slide 19: Preliminary Results
Nearing the completion of the first Habitat Module
Second one planned to bring us to full scale
Lots of ideas for adjustments for the second Habitat Module

## Slide 20: Conclusion
Purpose to gain insight and experience of our technology in a low risk and low cost environment
Improve procedures, experiments, and effectiveness of research as it pertains to human, robotic, and any other system interaction
Provide a more accessible and affordable facility for any entity that would benefit from the capabilities provided by this analog

## Slide 21: Acknowledgements
National Science Foundation's CAMP Program
Dr. Stephen K Robinson
My Fellow HRVIP Lab Members
URC, Specifically Lolita Adkins and Dr. Franz

## Slide 22
References
https://hrvip.ucdavis.edu/HRVIP_projects
https://solarsystem.nasa.gov/moons/in-depth/
https://www.planetary.org/space-missions
https://www.nasa.gov/directorates/spacetech/strg/stri/stri_2018/Habitats_Optimized_for_Missions_of_Exploration_HOME/
https://howthingsfly.si.edu/ask-an-explainer/how-much-fuel-would-it-take-shoot-rocket-out-atmosphere#:~:text=A%20good%20rule%20of%20thumb,a%20rocket's%20weight%20is%20fuel.
https://www.nasa.gov/mission_pages/station/expeditions/expedition30/tryanny.html

## Slide 23
Questions?